# Text boxes

NOTE:

Phone/TV: Allow approximately 8” of slack in cables in isolated compartment for front panel removal.

Phone: RJ11 phone jack can be replaced with a RJ45 jack.(RJ45 used for DSL internet, not available through Midwest)

5. Cable TV Jack: With nut removed form fitting, place long end of threaded fitting through the back of the deadfront and seat integral hex portion of shaft in to hex pocket. Place removable hex nut onto  the shaft protruding through the front of the deadfront and tighten securely.

Connect cable.

6. Telephone jack: Run phone cable through hole in deadfront pocket (through the back of the deadfront towards the front). Terminate phone wires to proper terminals on telephone jack. Insert phone jack into pocket on front of deadfront. Carefully align to the mounting screws with mounting holes in the pocket and tighten securely.

6. Re-install deadfront and restore power.

VATELTV Kit: Kit includes a Telephone/TV Compartment Barrier,

Twist Lock Telephone Jack, and cable TV jack.

VKTELTV1 Kit: Kit includes a Telephone/TV Compartment Barrier,

Deadfront with mounting plate for RJ11 & TV jack. One RJ11

Telephone jack, and one Cable TV jack.

VKTELTV2 Kit: Kit includes a Telephone/TV Compartment Barrier,

Deadfront with mounting plate for RJ11 & TV jack. Two RJ11

Telephone jack, and two Cable TV jack.

1. Turn off main power to the unit and remove deadfront panel.

2. For 2001 or later Dockmasters and Parkmates on a post and Dockmates on a post the conduit supplied in the kit can be cut to size and used.  For Parkmates on a post and Dockmates on a post make a 1.25” hole on the back of the unit.  For Dockmasters locate the 1.25” hole on the bottom of the unit next to the chamfer in the enclosure and 2.50” in from the front of the unit.

3. Install telephone/TV compartment barrier as shown in the above illustration, (ensure this barrier is installed at all times when telephone and/or TV jacks are installed and wired up.)

4. When installing the cable TV jack and/or the telephone jack,

you may have to drill a 3/8” dia. hole for the older style units,

through the deadfront using the drill point provided as a

locating position.

R02 5/18/01

MEPI136

UTELTV Kit: kit includes a telephone/TV Compartment Barrier, Twist Lock Telephone Jack, and cable TV jack.

UTEL Kit: Kit includes a telephone/TV compartment barrier, and a Twist Lock telephone jack.

UTV Kit: Kit includes a Telephone/TV compartment barrier, and a cable TV jack.

VATELTV Kit  - Telephone and TV Connection Kit

VKTELTV1 Kit - Telephone and TV Connection Kit

VKTELTV2 Kit - Telephone and TV Connection Kit

NOTES:

U = 2000 and early units

VA = 2001 and later Dockmates & Dockmasters

VK = 2001 and later Parkmates

KITS COVERD:

UTELTV Kit - Telephone and TV Connection Kit

UTEL Kit - Telephone Connection Kit

UTV Kit - TV Connection Kit

INSTALLATION INSTRUCTIONS FOR TELEPHONE/TV CONNECTIONS IN DOCKMATE/PARKMATE